The TAC - Tone Arm Connector

To support our tone-arm cable types D - 502 HYBRID (and D - 501 HYBRID and D - 501 SILVER HYBRID), The TAC is available. The D - 502 HYBRID is a flat shaped twin cable. To get a good grip on this cable, a special connector had to be made.
Its 5 contacts are 24 carat gold over silver over copper plated. The connector contacts with their standard 270° pin configuration are based in a Teflon disc. This disc can be adjusted in any angle related to the connector housing. This to set the optimal position related to the tone arm. There is enough space in the connector house to have the cable wires pushed in after soldering. The connector housing incorporates a 90° bend to combine vertical mounting and horizontal cable exit. Cable clamping is performed by tightening the rear-nut of this 3 part construction. (In case the housing of The TAC does not fit in the tone-arm socket, use sandpaper to slim the outer dimensions).

Colour: Black.
Cable entrance dimensions: 10.0 x 4.0 mm (w x h)
For optimal contact care we recommend our The SOLUTION contact fluid.

SME IV & SME V Right Angled Tonearm Connector

Clearaudio 5 pin Tonearm Connector

(Non Magnetic)

The increasing need for a high quality 5 Pin DIN connector has led us to the design of the Clearaudio 5 Pin DIN. A typical Clearaudio feature-rich product featuring excellent craftsmanship, non-magnetic materials and spring connectors.

The connector offers an 8.25 mm cable opening and compression collet, this allows for larger cables than the Cardas DIN. Solder cups on the contacts have been cut at an angle making it much easier to tin and solder the contact.

Deep Cryo Treated